## Slide 1: Box Breaker Game Project
EE319H Introduction to Embedded System Honors
By Daniel Yang

## Slide 2: Executive Summary
The game Box Breaker is played on a TI microcontroller interfaced with input and output hardware
The software implementation is done on Keil 5 IDE that includes sprite design, level design, and main file programming

## Slide 3: The game is the final project of Introduction to Embedded System Honors (EE319H) that must fulfill the minimum requirements
Hardware Requirements | Two buttons Slide potentiometer with ADC Speaker with DAC Liquid crystal display (LCD)
Software Requirements | Two interrupt service routines (ISR) Three sprites Score display Two languages

## Slide 4: Box Breaker is like Brick Breaker, but instead of the ball hitting the brick, the cookie is hitting the box
English or Spanish
3 levels
4 lives
Each box can take 4 hit
Pink Box contains a powerup

## Slide 5: TM4C123GXL Microcontroller is the brain of hardware design
All Hardware components are connected to the board
The board receives the data from input hardware
The software then process that data
Finally, the data is sent to the output hardware

## Slide 6: Two built-in buttons are used to change language and use power-up
PORT F0
PORT F4
Edge-triggered on the falling edge

## Slide 7: The slide potentiometer is an adjustable 10kΩ resistor that controls the paddle position
Microcontroller
Built-in 12-bit ADC0
Value n from 0 to 4095
d = 159 – 140 *n / 4095,
Where d is the position of the paddle

## Slide 8: Two output devices are interfaced with the microcontroller, an LCD and a speaker
The 128x160 ST7745 LCD is used to display the game
The 4-bit binary-weighted DAC converts PB0-3 value to current for the speaker to play sound

## Slide 9: C++ Classes are written to code each sprite
Cookie Class
Box Class
Paddle Class
Move
Draw
Power-up
Lose-hp
Draw
Move
Draw

## Slide 10: One function is written for each level to initialize a unique layout of boxes
  Each Level can have a maximum of 5 rows and 9 columns of boxes
  Box[5][9] 2D array is declared to represent each box sprite
  The if statement check is used to initialize certain Box Objects
  Uninitialized Box Objects will not become sprites
for (every row)
for (every col)
if (…)
initialize Box[row][col]

## Slide 11
The design of each level

## Slide 12: The game begins by prompting user to select a language
English is selected
Spanish is selected
Initialization
Display title Screen
Button
None pressed
Game engine
PF0 pressed
Change language output and language flag
PF4 pressed

## Slide 13: Game Engine updates each sprite’s movement, collision, and display every cycle
Semaphore
Call each Object’s Draw method
Semaphore = 0
Final Level
Win
Initialize next level
Box counter
potentiometer
Collision
Call Cookie Object Move method
Play “explosion” sound
Flip Cookie Object’s velocity variable
Semaphore = 1
Main
Initialization
Timer1A ISR
30 HZ
Call Paddle Object’s Move method
Enable Game Engine
1
0
0
> 0
yes
no
Call Box Object’s loseHp method
moved
no
no
yes

## Slide 14: Conclusion
  I briefly explained the hardware interface with the microcontroller and software design
  More levels and power-ups could be designed to make the game more interesting
  A difficulty system could also be implemented